Lock is probably OK but installation can be a bear.

June 1, 2016

Verified Purchase

This is the replacement for the discontinued 060-650. However;
- It has thicker strike bolts and comes with a new strike plate to accommodate this. Changing the strike plate is a major job on my RV, one has to open the aluminum door frame away from the coach frame to be able to do that, and that is not readily done on my RV, and probably many others. Fortunately the thread diameter on the striker bolts are identical on both new and old locks, and all line up perfectly, so removing the the striker bolts from the old lock and placing them in the new solved that problem, Notwithstanding the dire warning label.
- The lock does fit in the cutout made for the the discontinued 060-650, but it cannot be operated without making modifications to either the lock or the cut-out. It is designed using a a deadbolt activation system that obviously is common to other locks, and so has linkage attachment tabs that are not used on this particular lock. These extraneous and unused metal linkage tabs rotate out beyond the rear of the lock when activation of the deadbolt is attempted, and interfere with the door frame. The frame has to be chiseled our in a very awkward position to accommodate this, or you would have to Dremel off these tabs. Trimark needs to remove these tabs during fabrication of the lock.
- In my case the two halves of the lock could not be readily mated together. The shaft on the the deadbolt control could not go into the red plastic lever, the shaft itself was over-size. It took me an hour of careful filing to reduce the size of the shaft until it would slide into the red plastic actuator, using a permanent marker pen as machinists blueing dye. It was the metal shaft not the actuator. The other shaft of the latch bolt control slid into the this actuator OK, and this shaft would not slide into the other actuator. I am not being neurotic here, If I forced it on to about 3/4's home, I had to lever the halves apart with screw drivers. It would have made taking the lock off the door for any reason unnecessarily difficult and the operating the deadbolt stiff. Quality Control, Trimark, Quality Control!

The internal design is completely different to the 060-650, and I hope Trimark has solved the problem of the latch bolt cracking through and flying out, on opening the door if you're lucky, and on closing the door if you are unlucky. However I will still use this new latch by holding the lever out and letting it in slowly, and not letting it snap into place, like I wish I had known was necessary with the old lock.