ACE 30.1 REMOVE KITCHEN WINDOW VALENCE AND VENETIAN BLINDS

- Remove two screws that are easily visible on two metal support brackets.  The screws hold the valence in position over the kitchen window.  Once the screws are out the valence can be slid out and away from the window.

- To remove the venetian mini blind unit first raise the blind slats by hand to the support bar and then use a slim flat blade screwdriver and insert it vertically from below, into the center slot of the clear plastic retainer clips. Pull each clear clip straight out from their respective wall mounting bracket about ¼ inch.  Lift up slightly on each clear plastic retainer clip tab with the screw driver so they lock in the slightly upright “released” position and then gently remove screw driver. Roll the venetian blind top bar down (It may roll out and down by itself when the clear clips are both released), while lifting up slightly at the rear to remove the venetian blind unit from the two support brackets.   Lay the venetian blind unit down on the counter and you don’t have to remove the tension strings screwed to the lower wall on either side of the blind.  Use care not to damage the strings.  Replacement is the opposite of removal.